## Slide 1: Introduction

## Slide 2
An Instruction – The command given to the computer to perform a specified operation on given data.
Instruction set of a microprocessor is a collection of the instructions that the microprocessor is designed to execute.
Instructions are classified into groups.

## Slide 3: Instruction Group
Data Transfer Group – Used to transfer data from one register to another register, from memory to register or register to memory. When an instruction of data transfer group is executed, data is transferred from the source to the destination without altering the content of the source. eg:- MOVE A, B
Arithmetic Group – Performs arithmetic operations such as addition, subtraction, increment or decrement of the content of a register or memory. Eg:- ADD, SUB

## Slide 4
Logical Group – Performs logical operations such as AND, OR, compare, rotate etc. eg:- CMP
Branch Control Group – Includes the instructions for conditional and unconditional jump, subroutine call and return, and restart. eg:- JMP
I/O and Machine Control Group – Includes the instructions for input/output ports, stack and machine control. eg:- PUSH, POP, IN, OUT